## Slide 2
An ISP has requested a block of 1000 addresses. Since 1000 is not a power of 2, 1024 addresses are granted. The prefix length is calculated as n = 32 − log21024 = 22. An available block, 18.14.12.0/22, is granted to the ISP. It can be seen that the first address in decimal is 302,910,464, which is divisible by 1024.
Example 18.4
18.2

## Slide 3
In classless addressing, an address cannot define the block the address belongs to. For example, the address 230.8.24.56 can belong to many blocks. Some of them are shown below with the value of the prefix associated with that block.
16, 20, 26, 27, 29, 31
Example 18.3
18.3

## Slide 4: 3 levels of hierarchy - Subnetting
Large Block of Address
  Clusters of Networks (Subnet)
  Divide the address between subnets
Rest of world will see as one-entity
  Router connects organization to rest of world
  Router routes to appropriate subnets
Organization – Own mask, each subnet – subnet-mask

## Slide 5: Designing Subnets
Sub-networks design
  Total no of address granted to organization is N
  Prefix length of each sub-network nsub
  Assigned no of address to each sub-network is Nsub
No of address in each sub network should be power of 2
Prefix length of each subnetwork nsub = 32 - log2Nsub
Starting Address in each subnetwork divisible by Number of address in that subnetwork
(First Assign Address to larger subnetworks)

## Slide 6
An organization is granted a block of addresses with the beginning address 14.24.74.0/24. The organization needs to have 3 subblocks of addresses to use in its three subnets: one subblock of 10 addresses, one subblock of 60 addresses, and one subblock of 120 addresses. Design the subblocks.
Example 18.5
Solution
There are 232– 24 = 256 addresses in this block. The first address is 14.24.74.0/24; the last address is 14.24.74.255/24. To satisfy the third requirement, we assign addresses to subblocks, starting with the largest and ending with the smallest one.
18.6

## Slide 7
a. The number of addresses in the largest subblock, which requires 120 addresses, is not a power of 2. We allocate 128 addresses. The subnet mask for this subnet can be found as n1 = 32 − log2 128 = 25. The first address in this block is 14.24.74.0/25; the last address is 14.24.74.127/25.
b. The number of addresses in the second largest subblock, which requires 60 addresses, is not a power of 2 either. We allocate 64 addresses. The subnet mask for this subnet can be found as n2 = 32 − log2 64 = 26. The first address in this block is 14.24.74.128/26; the last address is 14.24.74.191/26.
Example 18.5 (continued)
18.7

## Slide 8
c. The number of addresses in the smallest subblock, which requires 10 addresses, is not a power of 2. We allocate 16 addresses. The subnet mask for this subnet can be found as n3 = 32 − log2 16 = 28. The first address in this block is 14.24.74.192/28; the last address is 14.24.74.207/28.
Example 18.5 (continued)
If we add all addresses in the previous subblocks, the result is 208 addresses, which means 48 addresses are left in reserve. The first address in this range is 14.24.74.208. The last address is 14.24.74.255. We don’t know about the prefix length yet. Figure 18.23 shows the configuration of blocks. We have shown the first address in each block.
18.8

## Slide 9
Figure 18.23: Solution to Example 4.5

## Slide 10
Figure 18.24: Example of address aggregation

## Slide 11
Figure 18.24 shows how four small blocks of addresses are assigned to four organizations by an ISP. The ISP combines these four blocks into one single block and advertises the larger block to the rest of the world. Any packet destined for this larger block should be sent to this ISP. It is the responsibility of the ISP to forward the packet to the appropriate organization. This is similar to routing we can find in a postal network. All packages coming from outside a country are sent first to the capital and then distributed to the corresponding destination.
Example 18.6
18.11

## Slide 12
Figure 18.22: Network address

## Slide 13
Figure 22.5 Simplified forwarding module in classless address
In classless addressing, we need at least four columns in a routing table.

## Slide 14
Figure 18.32: Simplified forwarding module in classless address

## Slide 15
In classless addressing, we need at least four columns in a routing table.
Note

## Slide 16: Subnetting – Ex 2
Organization Block 17.12.14.0/26
  64 address
3 offices – to divide sub-blocks
  1st office – 32 address
  2nd office – 16 address
  3rd office – 16 address

## Slide 17: Subnetting – Ex 2
Organization Block 17.12.14.0/26
  64 address
3 offices – to divide sub-blocks
  1st office – 32 address
  2nd office – 16 address
  3rd office – 16 address
/n = 26, /n1 = 27 , /n2=28, /n3=28

## Slide 18
Figure 19.8 Three-level hierarchy in an IPv4 address

## Slide 19
Figure 19.7 Configuration and addresses in a subnetted network

## Slide 20: Subnetting – Ex 2
  Don’t get confused with this Forouzan’s Example diagram shown in previous slide
  Last address in that subnet is assigned to a system which ideally is wrong. (However total number of addresses in that subnet is correct)
  Router is assigned one of the IPs in that subnet to one of it’s interface since it identifies to which subnet it has to forward the packet to.
  Router will take decision by masking the Destination address based on prefix length to obtain Network portion and redirect to that subnet interface