## Slide 1: Module 5 – Network Layer IP Addressing
Jayavignesh
Asst Professor
SENSE

## Slide 2: OUTLINE
Functionalities of Network Layer
Internet Protocol
IPv4 Addressing (Logical, Global, Unique, Hierarchical)
Address Space, Notations
Classful Addressing
Subnetting
Classless Addressing
Network Address Translation (NAT)

## Slide 3: Functions of Network Layer
Source to Destination Delivery of Datagrams via multiple networks. (Host To Host Communication)
Internet Protocol (IP)
  Connectionless protocol
  Relaying datagrams across network boundaries. (Internetworking).
  Host Addressing to identify device
  Biggest Challenges
    Addressing: where should information be directed to?
    Routing: what path should be used to get information there?

## Slide 5
Figure 18.1: Communication at the network layer

## Slide 6: Hierarchical Addressing

## Slide 7
Levels of hierarchy in Telephone Numbering
Hierarchical addressing solves the problem of devices communicating across networks of networks

## Slide 8: IP Addressing Structure
Dotted decimal structure of a binary IP address

## Slide 9
An IPv4 address is 32 bits long.
Note
Uniquely and universally defines the connection of a device (for example, a computer or a router) to the Internet.

## Slide 10
Unique – Each address defines one & only one connection to Internet
Note
* 2 devices can never have same address at same time *
* Address may be assigned to a device for a time period and then taken away and assigned to another device *

## Slide 11
The address space of IPv4 is 232 or 4,294,967,296.
Note

## Slide 12
Figure 19.1 Dotted-decimal notation and binary notation for an IPv4 address

## Slide 13: IP Addressing Structure

## Slide 14: IP Addressing Structure

## Slide 15: IP Addressing Structure
Convert decimal to 8-bit binary

## Slide 16
Change the following IPv4 addresses from binary notation to dotted-decimal notation.
Example 19.1
Solution
We replace each group of 8 bits with its equivalent decimal number and add dots for separation.

## Slide 17
Change the following IPv4 addresses from dotted-decimal notation to binary notation.
Example 19.2
Solution
We replace each decimal number with its binary equivalent

## Slide 18
Find the error, if any, in the following IPv4 addresses.
Example 19.3
Solution
a. There must be no leading zero (045).
b. There can be no more than four numbers.
c. Each number needs to be less than or equal to 255.
d. A mixture of binary notation and dotted-decimal notation is not allowed.

## Slide 19
In classful addressing, the address space is divided into five classes:
A, B, C, D, and E.
Note

## Slide 20
Figure 18.17: Hierarchy in addressing

## Slide 21
Figure 19.2 Finding the classes in binary and dotted-decimal notation

## Slide 22
Figure 19.2 Finding the classes in binary and dotted-decimal notation

## Slide 23: IP Address Classes (Cont.)
The 5 IP classes are split up based on the value in the 1st octet:

## Slide 24: Network/Host Portions
The 32 bits of the IP address are divided into Network & Host portions, with the octets assigned as a part of one or the other.
Network & Host Representation
By IP Address Class
Class
Octet1
Octet2
Octet3
Octet4
Class A
Network
Host
Host
Host
Class B
Network
Network
Host
Host
Class C
Network
Network
Network
Host

## Slide 25
Find the class of each address.
a. 00000001 00001011 00001011 11101111
b. 11000001 10000011 00011011 11111111
c. 14.23.120.8
d. 252.5.15.111
Example 19.4
Solution
a. The first bit is 0. This is a class A address.
b. The first 2 bits are 1; the third bit is 0. This is a class C address.
c. The first byte is 14; the class is A.
d. The first byte is 252; the class is E.

## Slide 26
Number of blocks and block size in classful IPv4 addressing

## Slide 27: Specific Rules
Each Network is assigned a network address & every device or interface (such as a router port) on the network is assigned a host address.
There are only 2 specific rules that govern the value of the address.
A host address cannot be designated by all zeros or all ones.
These are special addresses that are reserved for special purposes.

## Slide 28: Class A Addresses (Cont.)
There are 16,777,214 Host addresses available in a Class A address.
To compute the number of hosts available in any of the class addresses, where “n” represents the number of bits in the host portion:
(2n – 2) = Number of available hosts
Class A address uses 7 bits to designate network,
(27 – 2) = 126 or there can be 126 Class A Networks. (Number of Class A networks)

## Slide 29: Class A Addresses (Cont.)
There are 128 Class A Network Addresses,
but because addresses with all zeros aren’t used & address 127 is a special purpose address,
126 Class A Networks are available.

## Slide 30: Class B IP Addresses (Cont.)
So how many Class B Networks can there be?
Using our formula, (214 – 2), there can be 16,382 Class B Networks & each Network can have (216 – 2) Hosts, or 65,534 Hosts.

## Slide 31: Special Addresses
A few addresses are set aside for specific purposes.
Network addresses that are all binary zeros, all binary ones & Network addresses beginning with 127 are special Network addresses.

## Slide 32: Special Addresses (Cont.)

## Slide 33: Classify and Define IPv4 Addresses

## Slide 34
Figure 18.18: Occupation of the address space in classful addressing

## Slide 35
In classful addressing, a large part of the available addresses were wasted.
Note
Internet Corporation for Assigned Names & Address (ICANN)

## Slide 36
Default masks for classful addressing
Mask can help us to find the netid and the hostid. (32 bit of contiguous 1 & 0’s)
/n notation – Classless Addressing (Classless Interdomain routing)

## Slide 37: Subnetting
Say Divide Large Block of Class A & B
  Several contiguous groups
  Assign Each group to smaller networks
  Subnets
  Introduced in Classful addressing
  Increases the number of 1s in mask
  Ex : Class A network divided into 4 subnets. Prefix Length nsub = 10

## Slide 38: Supernetting
Time came when A & B depleted 
Demand for mid-size blocks
But not meet requirements
Say 1000 address
  4 Class C blocks to create one supernetwork
Classless eliminated need to supernetting

## Slide 39
Classful addressing, which is almost obsolete, is replaced with classless addressing.
Note

## Slide 40: Classless Addressing
Overcome Address Depletion
No concept of classes
Address granted in blocks retained (variable length prefix)
  Depending on Requirement
  Classful is special case of Classless addressing

## Slide 41
In IPv4 addressing, a block of addresses can be defined as
x.y.z.t /n
in which x.y.z.t defines one of the addresses and the /n defines the mask.
Note

## Slide 42
Figure 18.20: Slash notation (CIDR)

## Slide 43
Figure 18.21: Information extraction in classless addressing
Set all suffix bits
to 1s
Set all suffix bits
to 0s

## Slide 44
The first address in the block can be found by setting the rightmost 32 − n bits to 0s.
Note

## Slide 45
The last address in the block can be found by setting the rightmost 32 − n bits to 1s.
Note

## Slide 46
The number of addresses in the block can be found by using the formula 232−n.
Note

## Slide 47
A classless address is given as 167.199.170.82/27. We can find the above three pieces of information as follows. The number of addresses in the network is 232− n = 25 = 32 addresses. The first address can be found by keeping the first 27 bits and changing the rest of the bits to 0s.
Example 18.1
The last address can be found by keeping the first 27 bits and changing the rest of the bits to 1s.
18.47

## Slide 48
Alternate way to find the same for 167.199.170.82/27 using the mask. The mask in dotted-decimal notation is 256.256.256.224 The AND, OR, and NOT operations can be applied to individual bytes
Example 18.2
18.48

## Slide 49: Classless Address Blocks Allocation
The addresses in block must be contiguous, one after another.
2. The number of requested addresses (N) in a block must be a power of 2.
  N=232-n (or)
  n = 32 – log2N
3. The first address must be evenly divisible by the number of addresses.

## Slide 50
A block of 16 addresses is granted to a small organization. We know that one of the addresses is 205.16.37.39/28. What is the first address in the block?
Solution
The binary representation of the given address is
11001101 00010000 00100101 00100111
If we set 32−28 rightmost bits to 0, we get
11001101 00010000 00100101 0010000
or 205.16.37.32.
Example 19.6

## Slide 51
A block of 16 addresses granted to a small organization
Say one of the addresses is 205.16.37.39/28

## Slide 52
We can see that the restrictions are applied to this block. The addresses are contiguous.
The number of addresses is a power of 2 (16 = 24), and the first address is divisible by 16.
The first address, when converted to a decimal number, is 1,720,193,680 , which when divided by 16 results in 107,512,105
Example 19.5

## Slide 53
Find the last address for the block
Solution
The binary representation of the given address is
11001101 00010000 00100101 00100111
If we set 32 − 28 rightmost bits to 1, we get
11001101 00010000 00100101 00101111
or
205.16.37.47
Example 19.7

## Slide 54
Find the number of addresses
Example 19.8
Solution
The value of n is 28, which means that number of addresses is 2 32−28 or 16.

## Slide 55
Another way to find the first address, the last address, and the number of addresses is to represent the mask as a 32-bit binary (or 8-digit hexadecimal) number. This is particularly useful when we are writing a program to find these pieces of information. the /28 can be represented as
11111111 11111111 11111111 11110000
(twenty-eight 1s and four 0s).
Find
a. The first address
b. The last address
c. The number of addresses.
Example 19.9

## Slide 56
Solution
a. The first address can be found by ANDing the given addresses with the mask. ANDing here is done bit by bit. The result of ANDing 2 bits is 1 if both bits are 1s; the result is 0 otherwise.
Example 19.9 (continued)

## Slide 57
b. The last address can be found by ORing the given addresses with the complement of the mask. ORing here is done bit by bit. The result of ORing 2 bits is 0 if both bits are 0s; the result is 1 otherwise. The complement of a number is found by changing each 1 to 0 and each 0 to 1.
Example 19.9 (continued)

## Slide 58
c. The number of addresses can be found by complementing the mask, interpreting it as a decimal number, and adding 1 to it.
Example 19.9 (continued)

## Slide 59
The first address in a block is normally not assigned to any device; it is used as the network address that represents the organization to the rest of the world.
Note

## Slide 60
Figure 19.4 A network configuration for the block 205.16.37.32/28